### Removal & Installation

V-bank cover, ignition coil and related components—GS350

Click to Enlarge

- Before servicing the vehicle, refer to the Precautions section.

- Disconnect the negative battery cable. Wait at least 90 seconds before performing any other work.

- Remove cool air intake duct seal.

- Remove the right and left engine room side covers.

- Remove V-bank cover.

Disconnect the ventilation hose at the cylinder head—GS350

- Disconnect the ventilation hose from the cylinder head.

Disconnect the MAF meter connector and clamp from the air cleaner—GS350

- Disconnect the Mass Air Flow (MAF) meter connector.

- Disconnect the clamp from the air cleaner.

Disconnect the VSV from the EVAP—GS350

- Disconnect the VSV from the EVAP.

- Disconnect the 4 clamps.

- Remove the hose clamp and air cleaner cap with air cleaner hose.

- Disconnect the 2 wire harness clamps.

- Disconnect the 6 ignition coil connectors.

- Remove the 6 bolts and 6 ignition coils.

To install:

- Install the 6 ignition coils with the 6 bolts and torque to 7 ft. lbs. (10 Nm).

- Connect the 6 ignition coil connectors.

- Connect the 2 wire harness clamps.

- Install the air cleaner cap with the air cleaner hose assembly with the 4 clamps and hose clamp.

NOTE

Be sure to install the air cleaner assembly so that the screw part of the hose clamp is as shown in the illustration.

- Install the VSV for EVAP to the air cleaner hose.

- Connect the MAF meter connector and clamp to the air cleaner.

- Connect the ventilation hose to the cylinder head cover with the clamp.

- Install V-bank cover.

- Install the right and left engine room side covers.

- Install cool air intake duct seal.

- Connect the negative battery cable.

- Perform system initialization procedure.