On the Generation TWO car  1995 on there are 2 EGR pipes.
A short one at the top and a longer one at the bottom.
They do NOT join together, which I thought they did to start with.
They individually connect to the back of the manifold separately.

(IF it is the top pipe blowing, you can see it all at the top of the engine, and I think it ie VERY easy to replace.)

NORMALLY, it is the bottom pipe that goes.
The mechanic advised me to let him do it, he also said I needed to drop the steering box and remove the CAT.

Basically the pipe has a flange at each end..  It connects from the top of the manifold feeder into the cat at the bottom end.  The top end it goes onto part of the back of the inlet manifold.

In principle, you just need a ratchet handle with a long extension, a U-joint and a 12mm socket, and patience.
Undo the bottom 2 bolts from the top of the engine under the hood.  Undo the Top 2 bolts from under the car on the floor.

I put the car onto ramps so that I could easily get under it.  And I had a box to stand on so I could do the bits under the hood.

See the pictures attached and read the next bits too.

Drain off about 5 litres of engine coolant.
Remove the "heating valve" that is attached to the bulkhead at the back of the inlet manifold.
Take off the vacuum pipe (small diameter) from the manifold that feed the brake servo. (might be different on your LH drive car, mine is RH drive of course).
Take off the water pipe (another small diameter pipe) from the back of the manifold.
Just bend these 2 pipes out the way, You should now have enough room to get closer to the top of the EGR pipe.

Do you have small hands, it would help.  And a helper too would save a lot of time.
I used a 1/2 inch ratchet, made up with a 9 inch extension, 1/2-3/8 reducer, 3 inch extension, 3/8-1/4 reducer and a UJ, then a 12mm socket. I would a little tape round the UJ so it was prevented from falling over to 90 degrees and encouraged to be mostly straight.  I might have been just better off with a wobbly joint, next time! (yup, I would do it again).

I chose to use a six sided socket, I really DID NOT want to risk rounding the nuts at all.

Send your helper under the car, feed the socket and extension down to him and ask them to position the socket onto the nut that you can just see.  Make sure they have their hands clear, just in case the socket slips off.  A quarter turn and the nut should be free, just wind it off, no washer.  At the bottom end of the EGR pipe, both of these are nuts.  Mine came off easy and there was no rust.

The other bottom nut was harder.  I used a 1/4 inch 12mm socket and a baby 4 inch ratchet.  There is no room to lever it with your hand.  It is right by the steering box, but yours is probably on the other side???  My baby ratchet has a hole in the end of it.  I tied on some cord and threaded it up into the engine bay towards the radiator.  I yanked on the cord to start the nut off, easy once it was started.

Same principle for the top of the EGR pipe, but in reverse.
You go under the car and the helper is up top.
As I did not have a helper, I put a piece of string around the neck of my socket, see pictures..  I needed the wire noose, so that it did not wind up the string.

I remember for the top bolts (yes bolts with washers that don't fall off) you have to route the socket and extension bar a different way to get to each bolt.

I also used a magnetic pick up stick to make sure the nut do not fall into some where where it could not be retrieved from when doing the top 2 nuts.

The pipe will come out the bottom of the car and you will see the damage, soot from the blowing and probably very weak at the joint.  Mine was only held together in a small place, right at the end of the concertina bit.

Clean up the manifold ends that the new pipe will attach to, I just used a clean rag.

Make sure that the new pipe will fit on, I do not think you want to bend it (they say you have to bend a generation ONE pipe to get that on).  Mine went on easily, and came out again easily.

There is a thin stainless steel gasket that will clip onto the top end flange of the new pipe.
There is a more normal metal gasket to go onto the bottom end, which fits over the 2 studs.

Put the new EGR pipe on and tighten them up as much as you can.

Good luck and let me know if you need any more help.

Please DO ask questions and I will expand this explanation ready for posting on the site.

Look at the other pictures and have a think about it.

I would do it again with out hesitation, I had to do it on my own and it only took 6-8 hours, no rushing, just pottering really and all that money saved.

WOW WOW WOW, it is SO quiet now, even more of a joy to glide around in.

Good luck.

Simon.

PS, and the comfort of a second car, just in case, helped me too.
I'm doing the cam timing belt next, 12ok miles is just up.