HERE ARE THE SPECIFIC CORRECT INSTRUCTIONS FOR PROGRAMMING YOUR LEXUS LX THREE BUTTON KEYLESS REMOTE. MARKINGS ON THE BACK OF KEY ARE AS FOLLOWS: FCC ID-HYQ1512V CANADA: 1551 102 539 RSS-210 DENSO

1. SHUT ALL DOORS. FROM OUTSIDE OF VEHICLE, USING MASTER REMOTE KEY, LOCK ALL DOORS, AND THEN PRESS UNLOCKS BUTTON ONCE TO UNLOCK DRIVER DOOR ONLY. OPEN DRIVERS DOOR, SIT IN SEAT, PUT MASTER KEY ASIDE. KEEP DRIVERS DOOR OPEN..ALL OTHER DOORS MUST BE SHUT.
2. PLACE NEW KEY IN THE IGNITION (DONT TURN IT) AND THEN REMOVE IT. (THIS SOULD ONLY TAKE YOU JUST A COUPLE SECONDS TO PUT IT IN AND PULL IT OUT).

WITHIN 40 SECONDS

3. MANUALLY LOCK AND UNLOCK THE DRIVER DOOR 5 TIMES.THIS IS ACTUALLY 10 MOVENTS OF THE LOCK BUTTON ITSELF. MANUALLY MOVE THE LOCK BACK AND FORTH..DONT USE THE ELECTRONIC BUTTON ON THE DOOR ARMREST. SOME INSTRUCTIONS TELL YOU TO USE THE ARMREST BUTTON TO LOCK/UNLOCK ELLECTRONICALLY BUT I DID IT MANUALLY AND IT WORKED FOR ME. INTERVALS BETWEEN LOCK AND UNLOCK SHOULD BE AT LEAST A SECOND DONT DO IT TOO FAST.
4. CLOSE DRIVERS DOOR AND RE OPEN FROM THE OUTSIDE. SIT IN SEAT.

WITHIN 40 SECONDS


5. AGAIN MANUALLY LOCK AND UNLOCK THE DRIVERS DOOR 5 TIMES. (TEN MOVEMENTS OF THE TOGGLE).
6. INSERT THE KEY INTO THE IGNITION. TURN TO ON FOR ONE SECOND THEN TO OFF AND REMOVE THE KEY. (IF YOU HAVE DONE EVERYTHING PROPERLY TO THIS POINT THE LOCKS WILL THEN LOCK AND UNLOCK BY THEM ONCE TO TELL YOU THAT YOU HAVE SELECTED ADD A KEY MODE.)

WITHIN 40 SECONDS

7. SIMULTANEOUSLY PRESS AND HOLD KEY LOCK AND UNLOCK FOR A MAXIMUM OF 1.5 SECONDS. (THIS IS WHERE MOST PEOPLE GO WRONG IF YOU HOLD BOTH BUTTONS DOWN TOO LONG .3.4.5.SECONDS.YOU HAVE MESSED UP THE PROCEDURE AND WILL PROBABLY HAVE TO START AGAIN FROM STEP ONE!!!)
8. WITHIN 3 SECONDS OF PRESSING BOTH BUTTONS IN STEP 7 PRESSES ANY KEY BUTTON FOR A MINIMUM OF 1 SECOND.

9. CLOSE DRIVERS DOOR PLACE KEY IN IGNITION AND START VEHICLE TURN OFF VEHICLE AND REMOVE KEY. (CLOSING DRIVERS DOOR AND INSERTING IGNITION KEY EXITS THE PROGRAMMING MODE) LOCKS SHOULD OPERATE PROPERLY WHEN PRESSING LOCK/UNLOCK BUTTONS. IF NOT START OVER.

NOTE: IF SYSTEM LOCKS AND UNLOCKS TWICE BY ITSELF AFTER STEP 8â€¦PROGRAMMING PROCEDURE HAS NOT BEEN COMPLETED.START OVER.

HOPE THIS IS HELPFUL BASICALLY MOST PEOPLE WERE HOLDING DOWN LOCK AND UNLOCK BUTTONS SIMULTANEOUSLY FOR TOO LONG IN STEP 7. DO IT QUICKLY .MAXIMUM 1.5 SECONDS. ALSO COUNT THE LOCK/UNLOCK TOGGLES CORRECTLY.