- REMOVE CENTER INSTRUMENT CLUSTER FINISH PANEL

| (a) | Apply protective tape to the areas shown in the illustration. |
| --- | --- |

Text in Illustration

| (b) | Insert moulding remover B and D as shown in the illustration. |
| --- | --- |
| (c) | Pull down moulding remover B in direction (1). With moulding remover B being pulled down, pull down moulding remover D in direction (2) to disengage the clip and guide. |
| (d) | Apply protective tape to the areas shown in the illustration. |

Text in Illustration

| (e) | Insert moulding remover B and D as shown in the illustration. |
| --- | --- |
| (f) | Pull down moulding remover B in direction (1). With moulding remover B being pulled down, pull down moulding remover D in direction (2) to disengage the clip. |
| (g) | Disengage the 2 clips and remove the center instrument cluster finish panel as shown in the illustration. |

- REMOVE ACCESSORY METER ASSEMBLY (w/o Navigation System) See: Instrument Cluster / Carrier\Service and Repair\Removal and Replacement\Accessory Meter\Removal

- REMOVE MULTI-DISPLAY ASSEMBLY (w/ Navigation System) See: Accessories and Optional Equipment\Navigation Display\Service and Repair\Removal and Replacement\Multi-Display\Removal

- REMOVE INSTRUMENT PANEL FINISH PANEL

| (a) | Pull the instrument panel finish panel in the direction indicated by the arrow to disengage the claw, 2 clips and 2 guides, and remove the instrument panel finish panel. |
| --- | --- |